## Slide 1
RAKSHAK.VYUH
Reads the handshake. Never the payload.
An offline analyzer that assesses an IPsec tunnel from the control plane alone.
Team Venom · SIH26160 · NTRO
The problem
An encrypted tunnel looks healthy from inside. The negotiation that decided its ciphers, its key exchange and its rekey policy travelled in clear before the first byte of payload was protected, and that traffic is discarded by every tool that watches the data path.
Teams and CERT-In assess tunnels by reading configuration files they were not given.

## Slide 2
How it works
1 Capture
A pcap file. No agent on the gateway, no traffic injection, no decryption key.
2 CipherLens
A from-scratch IKEv1 and IKEv2 dissector in Rust. Reads SA, KE, TS, ID, AUTH, NOTIFY and the nonce, including the length-framed substructures strongSwan actually sends.
3 AttackMap
Every negotiated suite is checked against RFC 8247, RFC 8221 and NIST SP 800-131A. Findings are rules, not opinions.
4 Evidence Ledger
Each finding is bound to a packet number and a SHA-256 chain over the capture, so any claim can be re-derived from the file.
5 Report
JSON, HTML, a CycloneDX CBOM, and swanctl remediation fragments that fix what was found.
Passive by construction. There is no code path in the engine that decrypts, injects or transmits.

## Slide 3
A corpus built from real gateways, not synthesised
Tunnel | Packets | ESP flows | IKE | Grade | Score | Findings
ikev1-aggressive-3des | 36 | 0 | 36 | F | 0 | 8
ikev1-aggressive-dh2048 | 36 | 0 | 36 | F | 0 | 7
ikev1-main-mode-3des | 50 | 0 | 50 | F | 0 | 7
ikev1-main-mode-des | 46 | 0 | 46 | F | 0 | 7
ikev2-dh1536 | 588 | 3 | 16 | C | 74 | 2
ikev2-legacy-integrity | 588 | 3 | 16 | B | 89 | 3
ikev2-modern | 592 | 3 | 16 | A | 99 | 1
ikev2-null-encryption | 590 | 3 | 16 | F | 0 | 5
ikev2-sha256-integrity | 588 | 3 | 16 | A | 99 | 1
ikev2-weak-dh | 588 | 3 | 16 | F | 39 | 4
ikev2-x25519 | 588 | 3 | 16 | A | 99 | 1
11 captures · 4,290 packets · 21 ESP flows · 280 IKE messages · 7 of 11 carrying real tunnel data
Every capture comes from two real strongSwan 5.9.13 gateways in Docker, negotiating for real, with seven labelled traffic classes pushed across the tunnel afterwards so the data path is populated and not merely implied.
One Security Association per direction, so the flow count is small. The packet count is what a passive observer actually sees, and it is where the data is.
Expectations were read from tcpdump and swanctl --list-sas on a live gateway, then pinned in tests. The parser is checked against them, never the other way round.

## Slide 4
What still leaks through the encryption
The claim we can actually support
ESP encrypts the payload. It does not encrypt packet size, direction or timing. A passive observer with no keys still has a feature vector, and the honest question is what that vector is worth.
So we measured it instead of claiming it.
Gradient-boosted trees, twelve features, 297 windows, leave-one-tunnel-out.
Whole tunnels held out, never random splits: windows from one capture were generated seconds apart, so a random split would report an accuracy nobody could reproduce.
Result
70% accuracy, held-out tunnel
43% majority-class baseline — the number to beat
97% of windows answered, 3% abstained
When the model is not confident it says so instead of guessing, and the abstention is counted against it. An evaluator who reports only accuracy on a model allowed to stay silent is reporting the easy half.
Three of the seven classes produced too few packets to label and are reported absent rather than quietly dropped. One class is never classified correctly, and the matrix below says so.
truth \ predicted | dns | icmp-bulk | icmp-int | video | abstain
dns | 0 | 1 | 0 | 5 | 2
icmp-bulk | 1 | 87 | 23 | 15 | 2
icmp-interactive | 0 | 14 | 106 | 0 | 1
video | 3 | 19 | 0 | 15 | 3
abstain | 0 | 0 | 0 | 0 | 0
The last column is the model declining to answer. The bottom row is that it never claimed to be sure when it was not.

## Slide 5
It finds what configuration review would miss
Worked example — the IKEv1 tunnel
Aggressive Mode put the gateway identity on the wire in the very first packet, unauthenticated. The proposal that carried it also asked for 3DES and a 1024-bit MODP group.
The peer never accepted the proposal, so no tunnel came up. The engine reports that refusal as a critical fact and scores the capture 0, rather than grading an association that does not exist.
Findings carry the packet number they were read from.
Across the corpus
MODP-1024 key exchange, critical
IKEv1 Aggressive Mode, critical
3DES, the SWEET32 birthday bound
NULL encryption, no confidentiality at all
SHA-1 integrity and PRF, demoted to MUST-
Harvest now, decrypt later, ranked by key exchange
Each is a rule bound to a citation, not a model's opinion.
VYU-002 · CRITICAL · read from packet #1
IKEv1 Aggressive Mode sends the peer identity in the clear
Aggressive Mode puts the identity and the hash on the wire unprotected, so a passive observer learns who peers with whom, and the pre-shared key becomes offline-crackable.
Standard: RFC 2407 §4.1; CVE-2018-5389 — IKEv1 PSK is offline-crackable

## Slide 6
Every claim is checkable, and the limits are stated
Evidence ledger
Findings are deduplicated across Security Associations and carry an occurrence count, so a capture with hundreds of retried handshakes does not report one fact hundreds of times.
The capture file is hashed with SHA-256 and bound into the chain. Tamper with the pcap and the ledger stops verifying.
Tests
137 tests pass, including a robustness suite that feeds truncated, corrupted and randomly mangled packets to the parser, and a regression test that pins the ESP flow grouping against tcpdump.
What it refuses to claim
If PFS state was not on the wire, the report says PFS was not observed. It does not infer it from the configuration.
A capture with no IKE in it explains itself instead of scoring clean.
The engine is deterministic. Where a judgement is genuinely uncertain we leave it out rather than invent a confidence number.
The dataset card lists seven limits, including the three traffic classes that produced too few packets to label. It ships with the corpus, not in an appendix.
And the split we keep
Every field the wire states outright is parsed. That is deterministic, it is auditable, and a rules engine does it better than a model ever will.
Machine learning runs beside it, on the one question a parser cannot answer: what is the shape of the traffic inside a tunnel it cannot read. It reports its confidence and abstains when unsure. No security verdict depends on it, and nothing is scored by a model.

## Slide 7
What we are asking for
A corpus with real labelled traffic, and a path to publish it openly.
The gap we hit
There is no public dataset of IKE handshakes paired with protected traffic. We built one for ourselves, from six negotiated tunnels.
It is small, and we say so. But it is real, reproducible with one command, and every label in it was verified against the gateway that produced it.
Releasing it is the fastest way to make everyone else's work checkable.
The path
Release the corpus and a dataset card with an explicit schema and stated limits.
Contribute it to the AIKosh open-source community as labelled IPsec negotiation data.
Extend coverage to IPv6, transport mode and rekey-triggered PFS, so the label space is complete rather than convenient.
Everything runs air-gapped. No cloud service, no telemetry, no account.